## Slide 1
Implementing the Mid-Atlantic
Corn and Wheat Algorithms
for GreenSeeker
Wade Thomason, VT
Steve Phillips, IPNI
Paul Davis, VCE retired
Josh McGrath, U of KY

## Slide 2: In-Season Remote Sensing
Satellite
Aerial photography
Ground-based Sensing

## Slide 3: In-Season Remote Sensing of Crop N Status

## Slide 4: In-Season Remote Sensing of N Crop N Status

## Slide 5
The vigor of the leaves and
the ratio of plant to soil
affect NDVI values
The vigor of the leaves and
the ratio of plant to soil
affect NDVI values
What the Sensor “Sees”

## Slide 6
Note that the biomass of each plant is observable in NDVI value

## Slide 7: Optical Sensor Values
NDVI
  Regardless of sensor is essentially a measure of biomass.
  NDVI = (NIR-VIS)/(NIR+VIS)

## Slide 8: GreenSeeker System

## Slide 9: Algorithm Development
Chart: INSEY
Painter, VA, 2000 | 1.37 | 3.014 | 3.5332 | 3.9946 | 4.2831 | 3.1582 | 2.9419 | 2.3795
Painter2, 2000 | 2.1112 | 2.4593 | 1.123 | 4.9411 | 4.5817 | 4.6042
Painter3, 2000 | 2.4871 | 2.5319 | 2.6439 | 1.6356 | 2.5879 | 2.2854 | 1.9045 | 1.9269 | 1.5796 | 2.6215 | 2.4198 | 1.4116
Suffolk, VA, 2000 | 1.8053 | 2.8823 | 1.8412 | 2.8592 | 2.0514 | 3.1156
Holland, VA, 2000 | 2.5814 | 3.2738 | 2.7353 | 4.1456 | 2.4019 | 3.6456 | 2.4489 | 2.7139 | 3.5302 | 4.0901 | 2.4275 | 2.8977 | 4.0131 | 4.2439 | 3.4276 | 3.1626 | 4.7226 | 3.231 | 4.0473 | 3.0857 | 3.5302 | 4.6499 | 4.2867 | 3.1712 | 5.0816 | 4.5089 | 4.3166 | 3.0772 | 2.6156 | 3.355 | 2.6498 | 2.4831
Painter, VA, 2001 | 2.4139 | 4.0438 | 3.6311 | 4.5389 | 4.704 | 4.5183 | 4.5802 | 5.1991 | 4.869 | 4.9309 | 4.9103 | 5.3435
Suffolk, VA, 2001 | 2.7505 | 2.7776 | 2.7505 | 2.6573 | 3.7512 | 4.403 | 3.649 | 3.7278 | 4.1443 | 4.5115 | 4.6836 | 4.3255 | 4.5483 | 4.3557 | 4.1518 | 5.2048
New Kent, VA, 2001 | 1.2859 | 0.90767 | 2.3751 | 2.2465 | 3.4264 | 2.2767 | 4.2812 | 2.6928 | 4.0845 | 1.6414 | 4.2131 | 2.3599 | 4.024 | 2.0801 | 2.7684 | 3.2449
Chatham, VA, 2001 | 3.1305 | 2.9716 | 2.5822 | 3.4801 | 3.6946 | 3.5595 | 3.8058 | 2.9795 | 3.9012 | 3.9727 | 3.6151 | 4.6162
Culpeper, VA, 2001 | 1.952 | 1.9036 | 2.2827 | 1.4519 | 2.807 | 2.9522 | 2.3231 | 1.7746 | 2.5408 | 3.1458 | 3.0813 | 1.6374 | 2.0811 | 2.0004 | 3.6459 | 3.904
Stuarts Draft, VA, 2001 | 2.6538 | 6.1867 | 3.4604 | 4.7671 | 5.7028 | 5.2753 | 6.2029 | 5.7512 | 5.0252 | 5.9528 | 5.3317 | 6.3561 | 6.5497 | 5.2833 | 6.832 | 6.953

## Slide 10: Algorithm Development
Chart: INSEY

## Slide 11: Response Index
N uptake in N-Rich area
N uptake in area to be Fertilized
= RI
60 lb N
40 lb N
= 1.5
Chart: N Rate, lb/ac
| 0 | 40 | 80 | 120 | 160 | 200 | 240
 | 50 | 90 | 120 | 150 | 180 | 190 | 185
 | 50 | 120 | 150 | 180 | 210 | 220 | 215
No in-season N
Add in-season N

## Slide 12: Wheat N Rate Algorithm

## Slide 13
Entering Required Information

## Slide 14: Virginia Wheat
High Reference
  At GS 25 (greenup)
Low Reference
  Only preplant N, no winter/greenup application
Days from planting to current
N rate applied at greenup
Maximum Yield
Maximum N Rate
NUE

## Slide 15
VIRGINIA APPROACH - Wheat

## Slide 16: Virginia Wheat Algorithm Inputs

## Slide 17: N-rich strip
  Trimble
    300 ft long
    Representative area of the field (not high or low)
    Rate equal to the highest rate needed by the crop for the season?
    May require a decreased
    pre-plant N rate
    Mark it!

## Slide 18: N-rich strip
  Trimble
    At appropriate time (Zakoks 30-32) measure NDVI from reference
    32 to 48 “ above canopy
    Full boom, ½ boom, handheld, manual entry

## Slide 20: Wheat Results – Coastal Plain
 |  | GreenSeeker | Standard | GreenSeeker | Standard
Year | Acres | N rate, lb/ac |  | Yield, bu/ac | 
2012 | 804 | 58.1 | 58.4 | 77.3 | 76.6
2013 | 1008 | 53 | 59 | 74.6 | 75.5
Avg Yield by N Application Method GS STD | 
86.75 | 74.16

## Slide 21: Effect of RI on N Rate
High | Low | RI
0.8 | 0.4 | 2.0
0.8 | 0.45 | 1.8
0.8 | 0.5 | 1.6
0.8 | 0.55 | 1.5
0.8 | 0.6 | 1.3
0.8 | 0.75 | 1.1

## Slide 22: Effect of RI on N Rate
High | Low | RI
0.8 | 0.4 | 2.0
0.8 | 0.45 | 1.8
0.8 | 0.5 | 1.6
0.8 | 0.55 | 1.5
0.8 | 0.6 | 1.3
0.8 | 0.75 | 1.1

## Slide 23: Effect of RI on N Rate
High | Low | RI
0.8 | 0.4 | 2.0
0.8 | 0.45 | 1.8
0.8 | 0.5 | 1.6
0.8 | 0.55 | 1.5
0.8 | 0.6 | 1.3
0.8 | 0.75 | 1.1

## Slide 24
As the High and Low References move together the response to N decreases.
RI is typically lower in the early season. Less N response/stress

## Slide 25: Effect of DFP on N rate
Parameters | 
Low Reference | 0.35
High Reference | 0.75
N Preplant | 10
Yield Goal | 210
Max N | 200
NUE | 50%
As DFP increases at a given RI the response to N decreases for lower NDVI
Higher NDVI’s need more N to achieve max yield

## Slide 26: General “Tips” on the VA Algorithms
What if I don’t have a high N reference?
  Use a “virtual” reference.
  Drive across the crop
  Note the highest NDVI value (sustained)
  Multiply by 0.9
  Enter that as “High” REF
  UNDERSTAND that what you just did was ASSUME that that difference is due to N

## Slide 27
“N-Rich” Strip

## Slide 28
Old fence-row

## Slide 29: General “Tips” on the VA Algorithms
What if I don’t have a LOW N reference?
  Use a “virtual” reference
  Drive across the crop
  Note the lowest NDVI value (sustained)
  Multiply by 1.2
  Enter that as “low” REF
  UNDERSTAND that what you just did was ASSUME that the low NDVI values were due to N deficiency

## Slide 30: General “Tips” on the VA Algorithms
Can I use the value from a high N reference from a neighboring field or from a different hybrid / variety?
  Absolutely NOT!

## Slide 31: “Tips” on the VA Wheat Algorithm
Very low “range” in N rate applied
  Low RI?
  Early in spring?
  High GS 25 N?
  Uniform stand?
  Low yield potential?

## Slide 32: “Tips” on the VA Wheat Algorithm
Very quick to max rate
  High RI?
  Early in spring?
  Low GS 25 N?
  Uniform stand?
  Overly optimistic yield potential?

## Slide 33: “Tips” on the VA Wheat Algorithm
The range of rates predicted by the system don’t match the number I had in mind.
  Ask yourself why
  Seek corroboration
  Tweak the inputs
  Build your own?

## Slide 34: Controlled Experiment
Conducted in Blacksburg
8 wooden boxes were built and filled with 1 of 4 soil type

## Slide 35: RX vs. Applied Rates
Notes: 55% of points are within 2 gal of prescribed rate
88% of points are within 5 gal of prescribed rate

## Slide 36: Sensor Summary
Requires that you are already comfortable with sidedressing the majority of your N
Install N rich strip and N deficient strip in each field
Understand that it’s not always right, but research indicates that it is correct more often than the flat rate you are currently using
There are different sensor technologies, but it’s really the algorithm that matters
Flat Rate

## Slide 37: Questions?